## Slide 1
From World-Model Case Generation to Self-Play RL Driving Policy
Building and Stress-Testing an Autonomous-Driving Intersection Simulator
Initial goal
world model
case generation
INCONCLUSIVE
Pivot
controlled simulator
+ PPO
IMPLEMENTED_AND_TESTED
Core system
V5 graph policy
qualified scope
PRODUCTION
Stress audits
pedestrians
longitudinal limits
DIAGNOSTIC_ONLY
Lane branch
V6 merge
negative result
REJECTED_CANDIDATE
• [PRODUCTION] V5 is the accepted simulator checkpoint, not road deployment.
• [REJECTED_CANDIDATE] Later V5.1/V6 candidates were not promoted.
• [SCRIPTED_ONLY] Merge and pocket demos validate infrastructure, not learned behavior.
WALK
traffic signals + pedestrians + queues
15-minute technical research presentation
1
Notes: Main message: The talk frames the internship as an evidence-driven arc: an oversized world-model idea was scoped into a controlled intersection simulator, a qualified V5 graph policy was produced for a declared simulator scope, and later branches produced useful but non-promoted negative results. Timing: 0:00–0:25 Speaker notes: The talk frames the internship as an evidence-driven arc: an oversized world-model idea was scoped into a controlled intersection simulator, a qualified V5 graph policy was produced for a declared simulator scope, and later branches produced useful but non-promoted negative results. Evidence / source boundary: Master context lines 7–13, 65–75, 95–109; results/status lines 5–13 and 115–124. Likely audience question: What does production mean here? Concise answer: It means the retained repository checkpoint/configuration that passed declared simulator gates, not road deployment or real-world certification.

## Slide 2
MAIN TALK
Introduction: the claim is deliberately bounded
2
The contribution is a rigorous, auditable simulator-policy program—not a claim of solved autonomous driving.
CLAIM DISCIPLINE
• Every major result is labeled by status: production, training-only, scripted-only, rejected, diagnostic, planned.
• Repository-confirmed results are separated from user-provided narrative and inconclusive history.
• Numerical claims are limited to handoff files and verified result/status matrices.
• Negative results are treated as controlled experiments that localize limits.
Status labels used as evidence qualifiers
PRODUCTION
TRAINING_ONLY
SCRIPTED_ONLY
LEARNED_PARTIAL
REJECTED_CANDIDATE
DIAGNOSTIC_ONLY
PLANNED
INCONCLUSIVE
Talk thesis
Build the simulator → audit policy ownership → improve realism → reject unsafe candidates → define lane-learning foundation.
Boundary: “production” is accepted simulator checkpoint/configuration, not real-world deployment.
Notes: Main message: The deck makes status labels part of each claim. This protects against overclaiming: V2.1 is training-only, merge/pocket demonstrations are scripted, V5.1/V6 are rejected candidates, and final banks were not run for failed candidates. Timing: 0:25–0:45 Speaker notes: The deck makes status labels part of each claim. This protects against overclaiming: V2.1 is training-only, merge/pocket demonstrations are scripted, V5.1/V6 are rejected candidates, and final banks were not run for failed candidates. Evidence / source boundary: Master context lines 3, 121–148; results/status lines 115–125; claim/evidence CSV. Likely audience question: Why so many labels? Concise answer: Because the project mixed simulator infrastructure, training support, learned policies, scripted oracles, and diagnostic audits. Without labels, the audience can easily misattribute scripted or training-only behavior to a promoted learned policy.

## Slide 3
PRIOR WORK / MOTIVATION
Background: why world models and adversarial cases were attractive
3
World models promise imagined rollouts; safety evaluation needs difficult, rare interaction cases.
• DreamerV3 shows the appeal of learning latent dynamics and improving behavior through imagined futures [R1].
• Autonomous-driving safety evaluation often searches for safety-critical scenarios rather than relying only on benign driving [R2].
• The initial internship idea was to combine these: learn a model, imagine futures, and generate adversarial cases.
• The handoff evidence does not verify a completed Dreamer implementation.
World-model RL
DreamerV3
Safety-critical
scenario search
Closed-loop
policy testing
Initial ambition:
world-model-based
adversarial case generation
Internship constraint:
adaptation + training + downstream generator
was too large for the timeline
INCONCLUSIVE
References [R1] DreamerV3; [R2] SafeBench. Dreamer implementation details are not repository-confirmed in the handoff.
Notes: Main message: This slide gives the research context. DreamerV3 motivates imagined-rollout world-model RL; SafeBench motivates systematic safety-critical scenario evaluation. The internship’s initial idea combined these, but the handoff explicitly says the Dreamer implementation itself is inconclusive in the repository evidence. Timing: 0:45–1:10 Speaker notes: This slide gives the research context. DreamerV3 motivates imagined-rollout world-model RL; SafeBench motivates systematic safety-critical scenario evaluation. The internship’s initial idea combined these, but the handoff explicitly says the Dreamer implementation itself is inconclusive in the repository evidence. Evidence / source boundary: Master context lines 7–9, 17–21; Q&A Q001–Q006; external references R1–R2. Likely audience question: Did DreamerV3 fail technically? Concise answer: No supported claim says that. The rigorous wording is that the direction was too broad for the internship timeline and no repository-confirmed Dreamer result is available in the handoff.

## Slide 4
PRIOR WORK / MOTIVATION
Background: multi-agent driving simulators shaped the final scope
4
The executed project fits a broader trend: efficient, structured, closed-loop learning environments for interaction.
• SMARTS, Nocturne, and Waymax emphasize multi-agent closed-loop interaction as a core AV learning problem [R3–R5].
• Lane-graph representations preserve topology and actor-map relations better than raw flattened summaries [R6].
• PPO is a practical on-policy actor-critic baseline for continuous-control policy optimization [R7].
• This internship intentionally chose a smaller, inspectable simulator instead of a high-fidelity stack.
Prior-work axis
Representative point
Project choice
Simulator
Waymax / SMARTS / Nocturne
Custom intersection
Scene encoding
Lane graphs / structured features
Ego graph 49/27/25
RL optimizer
PPO / actor-critic
Shared PPO policy
Evaluation
Closed-loop metrics
Hard promotion gates
Design principle used here
Prefer controlled causality and reproducible gates over broad but unevidenced capability claims.
Reference papers are listed in the appendix; they provide context, not claimed baselines for this project.
Notes: Main message: The project aligns with prior work on multi-agent driving simulation and graph-structured traffic representations. However, I do not frame this as a direct benchmark against Waymax, SMARTS, Nocturne, or LaneGCN. The project’s contribution is a controlled custom instrument for policy ownership and qualification. Timing: 1:10–1:35 Speaker notes: The project aligns with prior work on multi-agent driving simulation and graph-structured traffic representations. However, I do not frame this as a direct benchmark against Waymax, SMARTS, Nocturne, or LaneGCN. The project’s contribution is a controlled custom instrument for policy ownership and qualification. Evidence / source boundary: Technical methodology lines 13–17, 161–169; external references R3–R7. Likely audience question: Why not use an existing simulator? Concise answer: Existing simulators are powerful, but the internship needed full control over rules, rewards, event accounting, seed banks, and failure replay. The custom simulator made the evidence chain inspectable.

## Slide 5
PROJECT ARC
Internship objective and final scope
5
The final scope was a tractable version of the original theme: hard interaction cases under a controlled simulator.
• [INCONCLUSIVE] Initial goal: world-model adversarial case generation using DreamerV3.
• [IMPLEMENTED_AND_TESTED] Executed scope: four-way intersection simulator + shared PPO control stack.
• [PRODUCTION] Final retained artifact: V5 graph longitudinal policy for declared simulator matrix.
• [IMPLEMENTED_AND_TESTED] Extra foundation: lane topology, merge trajectory, V6 mechanics, and failure evidence.
Initial ambition
Executed core
Boundary
DreamerV3
world model
adversarial cases
Simulator
PPO
qualification
No real-road
no perception
no V6 promotion
USER-PROVIDED / INCONCLUSIVE
REPOSITORY-CONFIRMED
NO OVERCLAIM
Final research question
Can one shared learned policy produce longitudinal intersection behavior across vehicles, densities, signals, queues, turns, and pedestrians without a runtime acceleration shield?
Production = accepted simulator checkpoint/configuration, not road deployment.
Notes: Main message: The final scope is best explained as an evidence-bounded pivot. The original world-model direction stays in the story as motivation. The executed scope is repository-confirmed: a simulator, shared PPO stack, graph policy, and evaluation protocol. Timing: 1:35–2:00 Speaker notes: The final scope is best explained as an evidence-bounded pivot. The original world-model direction stays in the story as motivation. The executed scope is repository-confirmed: a simulator, shared PPO stack, graph policy, and evaluation protocol. Evidence / source boundary: Master context lines 7–13, 121–133; results/status lines 115–124. Likely audience question: Is the final system still related to adversarial case generation? Concise answer: Conceptually yes, because it stress-tests difficult interaction cases; code-wise no Dreamer/world-model case generator is verified in the handoff.

## Slide 6
PROJECT ARC
Initial world-model direction and pivot
6
The pivot was a scope-control decision: preserve the hard-case theme, change the experimental instrument.
• [INCONCLUSIVE] Original workflow: understand/modify DreamerV3, train a world model, use imagined rollouts for hard cases.
• [REPOSITORY-CONFIRMED] Handoff found no DreamerV3 code, checkpoint, training log, or result in inspected workspace.
• [IMPLEMENTED_AND_TESTED] New plan: implement simulator tasks directly and train a policy against explicit evaluation banks.
• Result: every claim could be reproduced, replayed, and rejected under gates.
Before pivot
DreamerV3 codebase
Latent world model
training
Imagined adversarial
case generator
Scope too large
for internship window
After pivot
Controlled simulator
Shared PPO policy
Seeded stress banks
+ promotion gates
INCONCLUSIVE
IMPLEMENTED_AND_TESTED
Safe wording: “scope-driven pivot,” not “Dreamer failed.”
Notes: Main message: This slide should be presented carefully. I can say the project began with a world-model/DreamerV3 direction and pivoted because the combined burden was too large. I cannot claim Dreamer training, implementation details, or measured failure. Timing: 2:00–2:25 Speaker notes: This slide should be presented carefully. I can say the project began with a world-model/DreamerV3 direction and pivoted because the combined burden was too large. I cannot claim Dreamer training, implementation details, or measured failure. Evidence / source boundary: Master context lines 7–21, 137–138; Q&A Q001–Q007. Likely audience question: Why not leave the Dreamer slide out entirely? Concise answer: Because it explains the internship arc and motivation, but it must be bounded as user-provided/inconclusive rather than repository-confirmed implementation.

## Slide 7
PROBLEM FORMULATION
Final research problem: parameter-sharing self-play RL
7
Each vehicle acts locally, but every vehicle is another copy of the same learned policy.
• [PRODUCTION] Each active vehicle receives its own ego-centered observation graph.
• [PRODUCTION] A single stochastic actor and critic are reused for all vehicles.
• [IMPLEMENTED_AND_TESTED] PPO aggregates samples from all active roles: leader, follower, turning, yielding, priority.
• [INCONCLUSIVE] “Self-play” here is shared-policy interaction, not a minimax opponent league.
WALK
traffic signals + pedestrians + queues
πθ(a|o)
shared actor
Vφ(o)
critic
per-ego observation
+ per-ego action
PPO rollouts
all active cars
Routes, signals, spawns, pedestrians, and legal/event semantics remain environment-owned.
Notes: Main message: The final problem is multi-agent partially observed control with parameter sharing. Each vehicle has a local graph observation, outputs its own action, and contributes a sample to one shared PPO update. This is why retention interference matters: a change that helps one role can hurt another. Timing: 2:25–2:50 Speaker notes: The final problem is multi-agent partially observed control with parameter sharing. Each vehicle has a local graph observation, outputs its own action, and contributes a sample to one shared PPO update. This is why retention interference matters: a change that helps one role can hurt another. Evidence / source boundary: Technical methodology lines 5–17; simulator/architecture lines 28–32; Q&A Q019–Q023. Likely audience question: Are all vehicles controlled by one global action? Concise answer: No. The policy parameters are shared, but observations and actions are per ego vehicle. The environment couples the outcomes through interaction.

## Slide 8
SIMULATOR
Simulator and multi-agent task setup
8
The simulator became the experimental instrument: controlled, replayable, and extensible.
• [IMPLEMENTED_AND_TESTED] Four-way intersection with route polylines, stop lines, lanes, spawns, and stable vehicle slots.
• [IMPLEMENTED_AND_TESTED] Signals include green, yellow, all-red, protected/permissive left, WALK, and right-on-red context.
• [IMPLEMENTED_AND_TESTED] Interactions include queues, pedestrians, vehicle footprints, collision/proximity events, and failure traces.
• [IMPLEMENTED_AND_TESTED] Supports headless rollouts, deterministic seeds, rendering, telemetry, and grouped qualification.
Research-scale intersection simulator
WALK
traffic signals + pedestrians + queues
Signals
Queues
Pedestrians
Collisions
Seeds
Research simulator, not photorealistic perception or certified traffic-engineering package.
Notes: Main message: I treat the simulator as an instrument, not a visualization. It controls routes, signals, pedestrians, geometry, legal/event semantics, and deterministic evaluation. That is what made causal debugging possible. Timing: 2:50–3:15 Speaker notes: I treat the simulator as an instrument, not a visualization. It controls routes, signals, pedestrians, geometry, legal/event semantics, and deterministic evaluation. That is what made causal debugging possible. Evidence / source boundary: Simulator/architecture lines 18–26, 93–97; master context lines 25–31, 49–53; Q&A Q013–Q018. Likely audience question: How realistic is the simulator? Concise answer: It captures interaction, signals, pedestrians, queues, collision geometry, and jerk-limited longitudinal dynamics, but it is not a perception stack, real-map system, or full vehicle dynamics model.

## Slide 9
SIMULATOR / METHODOLOGY
System boundary: what decides what?
9
Policy ownership was the central methodology correction: safe rollouts must be caused by the actor, not an override.
• [IMPLEMENTED_AND_TESTED] Early safety filters/reservation logic helped demonstrations but blurred attribution.
• [PRODUCTION] Formal V5 qualification disables runtime acceleration override.
• [PRODUCTION] Environment owns routes, legal state, event truth, and physics; policy owns acceleration choice.
• [TRAINING_ONLY] Prewarm/auxiliary targets operate only during optimization, not runtime inference.
Scenario/task sampler
exists / initial conditions
Intersection env + legal/event semantics
what is legal / what happened
Ego graph per active vehicle
what each agent observes
Shared actor-critic policy
runtime acceleration decision
Action scaling + jerk dynamics
what motion is feasible
Rewards, telemetry, qualification
what gets promoted
Claim rule
A safe trajectory is not automatically evidence of a safe policy.
Runtime action substitution is disallowed for promoted learned behavior; environment semantics are still engineered.
Notes: Main message: This is the core methodology correction. A safety shield can make trajectories safe while hiding a bad policy action. The final standard allows engineered environment semantics and training-only supports, but the actor must choose runtime acceleration in formal evaluation. Timing: 3:15–3:45 Speaker notes: This is the core methodology correction. A safety shield can make trajectories safe while hiding a bad policy action. The final standard allows engineered environment semantics and training-only supports, but the actor must choose runtime acceleration in formal evaluation. Evidence / source boundary: Simulator/architecture lines 5–16, 87–97; master context lines 35–37, 57–65; Q&A Q067–Q073. Likely audience question: Is production V5 completely unscripted? Concise answer: No. The simulator defines routes, legal semantics, signals, collisions, and physics. The precise claim is no runtime acceleration override in formal V5 qualification.

## Slide 10
TRAINING PROGRESSION
Training curriculum ladder
10
Capability was staged to isolate behaviors and detect retention failures.
• [IMPLEMENTED_AND_TESTED] Started with collision/progress, red-green signals, queues, yellow/all-red, stop/creep.
• [PRODUCTION] Promoted V5 combines pedestrian yield, left yield, right-on-red, and combined stress settings.
• [REJECTED_CANDIDATE] Later corridor prediction and V5.1 robustness did not replace V5.
• [SCRIPTED_ONLY]/[REJECTED_CANDIDATE] Lane infrastructure was validated; learned merge remained unsafe.
1
collision
+ progress
IMPLEMENTED
AND_TESTED
2
signals
red/yellow/all-red
PRODUCTION
3
queues
+ red creep
PRODUCTION
4
pedestrian
yield
PRODUCTION
5
left yield
+ ROR
PRODUCTION
6
combined
sparse/dense/stress
PRODUCTION
7
ped/V5.1
audits
REJECTED
CANDIDATE
8
lane/merge
V6 attempt
REJECTED
CANDIDATE
Promotion hierarchy
training-only / learned partial / rejected / production
Candidate usefulness ≠ promotion; failing any required group means non-promotion.
Notes: Main message: The ladder was both a simulator-feature ladder and a claim-discipline ladder. A stage could be implemented and tested without being promoted. The production endpoint is V5 combined longitudinal behavior; the later pedestrian and lane branches are not production replacements. Timing: 3:45–4:15 Speaker notes: The ladder was both a simulator-feature ladder and a claim-discipline ladder. A stage could be implemented and tested without being promoted. The production endpoint is V5 combined longitudinal behavior; the later pedestrian and lane branches are not production replacements. Evidence / source boundary: Training curriculum lines 5–23 and 27–45; brief/story lines 25–37. Likely audience question: Which rung is the production endpoint? Concise answer: V5 combined longitudinal intersection behavior under declared simulator gates. Pedestrian V2.1 and V6 are not production.

## Slide 11
EVALUATION
Evaluation protocol and qualification gates
11
Promotion required deterministic evaluation, separated seeds, no runtime action shield, and hard per-group gates.
• [PRODUCTION] Completion ≥ 90%; collision-event ≤ 1%; involved-vehicle ≤ 2%; other-violation ≤ 3%.
• [PRODUCTION] All 30 release-claim groups had to pass; not just average reward or completion.
• [IMPLEMENTED_AND_TESTED] Instrumentation parity and seed inventories protected replay and bank separation.
• [INCONCLUSIVE] Final reserved banks were not run for candidates that failed earlier gates.
Metric gate
Threshold
Meaning
Completion
≥ 90%
task success
Collision event
≤ 1%
one-shot crash pairs
Involved vehicles
≤ 2%
vehicle impact footprint
Other violations
≤ 3%
red/yield/timeout etc.
Promotion logic
Candidate must pass every required group under the exact runtime contract.
NO SHIELD IN FORMAL V5 QUALIFICATION
Hard gates prevent a high reward or completion rate from masking category regressions.
Notes: Main message: The key evaluation principle is multi-metric retention. Improvement in one metric did not justify promotion if another safety or legality metric regressed. This is why V5.1 and V6 negative results are meaningful rather than failures hidden by aggregate returns. Timing: 4:15–4:40 Speaker notes: The key evaluation principle is multi-metric retention. Improvement in one metric did not justify promotion if another safety or legality metric regressed. This is why V5.1 and V6 negative results are meaningful rather than failures hidden by aggregate returns. Evidence / source boundary: Results/status lines 5–13, 113–124; technical methodology lines 161–169; Q&A Q136–Q140. Likely audience question: Are these gates safety proofs? Concise answer: No. They are project-defined simulator qualification thresholds. Passing them qualifies the checkpoint for the declared matrix only.

## Slide 12
ARCHITECTURE
Architecture evolution: MLP to graph actor-critic
12
Variable traffic structure drove the move from flat vectors to typed graph attention and specialized modes.
• [IMPLEMENTED_AND_TESTED] Early shared two-layer tanh MLP consumed fixed per-car vectors.
• [PRODUCTION] V5 uses ego-centric graph observations and a custom typed graph-attention actor-critic.
• [PRODUCTION] Actor evolved to brake/creep/go mixture with residual adapters.
• [INCONCLUSIVE] No repository-confirmed Transformer policy stage.
• [REJECTED_CANDIDATE] V6 adds categorical lane intent over frozen V5 but was not promoted.
Discrete
concept
longitudinal
+ lateral choices
IMPLEMENTED
Shared MLP
2-layer tanh
Gaussian actor
IMPLEMENTED
Graph AC
49/27/25
typed attention
PRODUCTION
V5 mixture
brake / creep / go
residual adapters
PRODUCTION
V6 hybrid
LEFT/KEEP/RIGHT
+ residual
REJECTED
Why graph?
• traffic count varies
• more than one neighbor can matter
• front, conflict, route, signal relations differ
Custom graph-attention readout is not the same as a Transformer stage.
Notes: Main message: This architecture slide should emphasize why the graph was needed: flat summaries lose relational structure as traffic count and roles vary. The V5 production architecture is graph actor-critic plus a longitudinal mixture. A Transformer stage is explicitly inconclusive and should not be added. Timing: 4:40–5:10 Speaker notes: This architecture slide should emphasize why the graph was needed: flat summaries lose relational structure as traffic count and roles vary. The V5 production architecture is graph actor-critic plus a longitudinal mixture. A Transformer stage is explicitly inconclusive and should not be added. Evidence / source boundary: Architecture evolution lines 5–18, 21–52, 54–70, 84–101; master context lines 41–45; Q&A Q049–Q054. Likely audience question: Did you compare GNN and Transformer performance? Concise answer: No controlled Transformer comparison is preserved, and no repository-confirmed Transformer policy stage exists in the handoff.

## Slide 13
ARCHITECTURE
V5 graph observation schema: 49 / 27 / 25
13
Each controlled car sees an ego-centric, masked graph—not raw sensors and not full simulator state.
• [PRODUCTION] Ego vector: 49 features for motion, route, signal/legal, front-gap, yield and pedestrian timing.
• [PRODUCTION] Node features: up to 52 nodes × 27 features for vehicles and context entities.
• [PRODUCTION] Edge features: 25-D typed relations for front/back/adjacent/conflict/priority context.
• [PRODUCTION] Exact future signal countdown is not exposed; observation is structured, noise-free simulator state.
ego
49-D
vehicle
node 27-D
front / TTC
edge 25-D
lane/map
context
signal/legal
context
masked padded graph, max 52 nodes
Tensor
Dimension
Role
ego
49
motion + route + legal
node
52 × 27
agents + context
edge
25
typed relation
This is a privileged simulator abstraction, not camera/LiDAR perception.
Notes: Main message: V5’s input contract is a key technical result: 49-D ego vector, node vectors with a selected checkpoint max of 52 nodes, and 25-D typed edge features. It is rebuilt for each ego vehicle with relative coordinates and masks. Timing: 5:10–5:40 Speaker notes: V5’s input contract is a key technical result: 49-D ego vector, node vectors with a selected checkpoint max of 52 nodes, and 25-D typed edge features. It is rebuilt for each ego vehicle with relative coordinates and masks. Evidence / source boundary: Technical methodology lines 25–39; simulator/architecture lines 47–59; architecture evolution lines 21–29, 54–70; Q&A Q031–Q036. Likely audience question: Does the policy see the full simulator state? Concise answer: No. It sees an engineered local graph and context features, but not raw sensors or exact future signal countdown.

## Slide 14
ARCHITECTURE
V5 policy architecture and action interface
14
V5 is a graph actor-critic with specialized longitudinal modes; steering exists but is behaviorally inert.
• [PRODUCTION] Encoders map ego/node/edge inputs to 128-D embeddings; two graph-attention blocks update ego context.
• [PRODUCTION] Actor uses tanh-squashed brake/creep/go mixture with learned gate and residual adapters.
• [PRODUCTION] Deterministic evaluation selects gate argmax and component mean, not an average of incompatible modes.
• [PRODUCTION] Action 0 controls longitudinal acceleration; action 1 steering is retained but path-locked to zero at runtime.
graph
49/27/25
encoders
128-D
2 typed
graph-attn
blocks
critic
Vφ(o)
actor
πθ(a|o)
longitudinal mixture
brake
creep
go
gate
argmax at eval
two action coords
u: accel/brake
active
δ: steering
inert in V5
Do not claim V5 learned steering, lane changing, or free-form lateral control.
Notes: Main message: The final V5 architecture combines graph attention with a mode-aware longitudinal actor. The mixture head is not just a decorative detail: averaging brake and go can produce weak unsafe commands. The V5 interface retains steering, but Vehicle.step ignores steering and lateral offset, so it is path-locked. Timing: 5:40–6:10 Speaker notes: The final V5 architecture combines graph attention with a mode-aware longitudinal actor. The mixture head is not just a decorative detail: averaging brake and go can produce weak unsafe commands. The V5 interface retains steering, but Vehicle.step ignores steering and lateral offset, so it is path-locked. Evidence / source boundary: Architecture evolution lines 28–52, 54–70, 82–88; technical methodology lines 43–57; Q&A Q037–Q042 and Q051. Likely audience question: Why retain an unused steering output? Concise answer: It preserved interface compatibility during longitudinal development, but runtime geometry remained route-following and lateral control was not learned in V5.

## Slide 15
DYNAMICS
Jerk-limited kinodynamic dynamics
15
Simple kinematics made stopping labels too optimistic; jerk limits changed what was physically feasible.
• [IMPLEMENTED_AND_TESTED] Early kinematic model applied requested acceleration instantly.
• [PRODUCTION] `jerk_limited_v1`: dt = 0.2 s; a_max = 2.5 m/s²; comfortable braking = 4.0 m/s².
• [PRODUCTION] Acceleration change is limited by +3.0 m/s³ when increasing and 6.0 m/s³ when braking/decreasing.
• [IMPLEMENTED_AND_TESTED] Example: 2.0 m instant stop estimate vs 5.125 m actuator-aware distance.
action u ∈ [-1,1]
scale request
+2.5u / 4.0u
jerk clip
Δa ≤ JΔt
integrate
v, s
a_{t+1}=a_t+clip(a_req−a_t, ±JΔt)
v_{t+1}=clip(v_t+(a_t+a_{t+1})Δt/2, 0, 13.4)
s_{t+1}=s_t+(v_t+v_{t+1})Δt/2
instant
2.0 m
jerk-aware
5.125 m
v=4 m/s, a=+2 m/s², brake=4 m/s², J=6 m/s³
This is longitudinal kinodynamics, not full 6-DoF vehicle dynamics.
Notes: Main message: The dynamics change mattered because braking cannot appear instantly. When a car is already accelerating, the distance to ramp into braking can dominate a simple v squared over two b estimate. This changed dilemma-zone eligibility, brake labels, stopping-margin reward timing, and conflict feasibility. Timing: 6:10–6:45 Speaker notes: The dynamics change mattered because braking cannot appear instantly. When a car is already accelerating, the distance to ramp into braking can dominate a simple v squared over two b estimate. This changed dilemma-zone eligibility, brake labels, stopping-margin reward timing, and conflict feasibility. Evidence / source boundary: Master context lines 61–63; technical methodology lines 87–133; results/status lines 17–28; Q&A Q079–Q090. Likely audience question: Did the jerk model solve all stopping problems? Concise answer: No. It made feasibility more honest and exposed remaining insufficient-brake, gate-routing, and queue-chain failures.

## Slide 16
PEDESTRIAN MODELING
Pedestrian modeling: conservative default to predictive candidates
16
More selective pedestrian prediction improved targeted cases but did not clear production gates.
• [PRODUCTION] `crosswalk_wide_v1` remains the conservative production default.
• [REJECTED_CANDIDATE] V1 route-corridor prediction passed original checks but failed unused dense/stress holdouts.
• [REJECTED_CANDIDATE] V2 waiting-pedestrian activation fixed two late-clear traces but failed strict paired criteria.
• [TRAINING_ONLY] V2.1 imminent-WALK branch corrected seed 66827 but was not production-promoted.
crosswalk-wide
blocks broad
crosswalk
PRODUCTION
V1 corridor
route swept
occupancy
REJECTED
CANDIDATE
V2 waiting
possible
activation
REJECTED
CANDIDATE
V2.1 imminent
upcoming WALK
inside horizon
TRAINING
ONLY
Key methodological result
The visually better, less conservative model stayed rejected/training-only because holdout evidence did not justify replacing production.
V2.1 is training-only; production stayed crosswalk_wide_v1.
Notes: Main message: The pedestrian branch is a good example of disciplined non-promotion. Crosswalk-wide is conservative. V1/V2/V2.1 improve realism and targeted traces, but V1 and V2 regress holdouts or paired criteria, and V2.1 is only training support. Timing: 6:45–7:15 Speaker notes: The pedestrian branch is a good example of disciplined non-promotion. Crosswalk-wide is conservative. V1/V2/V2.1 improve realism and targeted traces, but V1 and V2 regress holdouts or paired criteria, and V2.1 is only training support. Evidence / source boundary: Master context lines 81–87; results/status lines 32–41; technical methodology lines 135–143; Q&A Q091–Q095. Likely audience question: Why keep the conservative default? Concise answer: Because the alternatives improved selected scenarios but introduced or exchanged failures in holdout or paired evaluations. Production evidence did not justify replacement.

## Slide 17
RESULTS
Production V5 result: qualified but bounded
17
V5 passed all 30 declared qualification groups under the exact simulator contract.
• [PRODUCTION] Checkpoint: `yield_kinodynamic_v5_combined_production.npz` with immutable SHA-256 identity.
• [PRODUCTION] Selected lineage: 51,200 PPO environment steps; only the ROR stage used 500 bounded prewarm steps.
• [PRODUCTION] Combined sparse/dense/stress groups passed 90/1/2/3 gates.
• Boundary: simulator release checkpoint, not real-road or perception robustness.
Group
Completion
Collisions
Involved
Other
Sparse 3l/12
99.72%
0.00%
0.00%
0.28%
Dense 3l/24
96.67%
0.63%
1.25%
1.88%
Stress 3l/36
92.22%
0.56%
1.11%
2.64%
30 / 30 GROUPS PASSED
Sparse completion
99.72%
Dense completion
96.67%
Stress completion
92.22%
Stress result is valid but close to gates; later unused audits exposed robustness gaps.
Metric order: completion / collision-event / collision-involved-vehicle / other-violation.
Notes: Main message: This is the headline production result. It should be shown with all four metrics, not only completion. V5 passed all 30 declared groups, but the stress group was close enough to gates that later holdout audits found robustness limits. That is why the result is strong but bounded. Timing: 7:15–7:50 Speaker notes: This is the headline production result. It should be shown with all four metrics, not only completion. V5 passed all 30 declared groups, but the stress group was close enough to gates that later holdout audits found robustness limits. That is why the result is strong but bounded. Evidence / source boundary: Master context lines 65–75, 113–119; results/status lines 5–13; Q&A Q056, Q136–Q140. Likely audience question: Was V5 trained entirely from scratch with PPO? Concise answer: No. The selected lineage includes 51,200 PPO environment steps and 500 bounded prewarm steps only in the ROR stage. The precise claim is PPO-trained learned runtime with no formal acceleration override.

## Slide 18
DIAGNOSTICS
V5.1 longitudinal robustness audit
18
The audit localized why a simple “drive faster” fix was unsafe.
• [DIAGNOSTIC_ONLY] V5 empty-green acceleration was policy-selected around 0.85 m/s², not actuator-limited.
• [DIAGNOSTIC_ONLY] A faster 1.5 m/s² reference earned slightly higher empty-road reward but collided in queue/turn probes.
• [DIAGNOSTIC_ONLY] 277 one-shot failures were categorized into queue-chain, brake, gate, late context, and reaction-delay classes.
• Lesson: longitudinal correction must be context-specific and retention-tested.
Stage 3B-0 failure taxonomy
Queue-chain
85
Insufficient brake
77
Mixture gate
74
Late env/obs
39
Reaction delay
2
Dominant insight
Not one scalar acceleration bug: failures came from queue dynamics, brake strength, gate routing, and late hazard exposure.
The taxonomy is diagnostic-only; counts come from a specific 90-seed diagnosis bank.
Notes: Main message: The audit changed the technical plan. It showed the conservative GO behavior was real, but a global acceleration increase would be unsafe. The failure categories motivated scoped gate/brake/retention experiments rather than broad coefficient changes. Timing: 7:50–8:20 Speaker notes: The audit changed the technical plan. It showed the conservative GO behavior was real, but a global acceleration increase would be unsafe. The failure categories motivated scoped gate/brake/retention experiments rather than broad coefficient changes. Evidence / source boundary: Master context lines 79–83; results/status lines 17–28; Q&A Q111–Q115. Likely audience question: Why not just increase the GO component? Concise answer: Because the empty-road reference was better, but global acceleration produced queue and turn safety problems. The correction must depend on context and pass retention gates.

## Slide 19
RESULTS / NON-PROMOTION
V5.1 PPO attempts: improved collisions, failed promotion
19
Every candidate failed at least one required gate or retention comparison, so V5 remained production.
• [REJECTED_CANDIDATE] Stage 3B-2A ran four mandatory-PPO candidates through 10,240 steps from immutable V5.
• [REJECTED_CANDIDATE] Stress collision events improved from 0.694% to 0.417% in probes.
• [REJECTED_CANDIDATE] Other violations rose to 3.19–3.33%, exceeding the 3% gate.
• [REJECTED_CANDIDATE] Balanced 40,960-step run and PPO-only fallback still failed stress or left/pedestrian retention.
• [INCONCLUSIVE] Final reserved bank was not run.
Candidate
Stress comp.
Coll.
Involved
Other
Decision
V5 baseline
94.17%
0.694%
1.389%
2.917%
pass
2,560
94.31%
0.417%
0.833%
3.194%
reject
5,120
94.31%
0.417%
0.833%
3.333%
reject
10,240
94.03%
0.417%
0.833%
3.333%
reject
NO V5.1 CHECKPOINT PROMOTED
Non-promotion rationale
Safety category regression matters more than isolated collision-column improvement.
Final bank status
Not run because earlier gates failed.
Negative result framed as retention discipline: no promotion when any required category regresses.
Notes: Main message: This slide should be delivered as an honest negative result. Some collision metrics improved, but the other-violation gate failed, and longer/balanced variants did not pass all retention requirements. Therefore the correct action was to keep V5 immutable. Timing: 8:20–8:55 Speaker notes: This slide should be delivered as an honest negative result. Some collision metrics improved, but the other-violation gate failed, and longer/balanced variants did not pass all retention requirements. Therefore the correct action was to keep V5 immutable. Evidence / source boundary: Master context lines 89–91; results/status lines 45–56; Q&A Q114–Q115 and Q139. Likely audience question: Was V5.1 safer overall? Concise answer: Not under the full gate set. It improved some collision metrics but regressed other required categories, so it was rejected.

## Slide 20
LANE / MERGE INFRASTRUCTURE
LaneSegment topology and merge infrastructure
20
The lateral branch first solved geometry and topology ownership before attempting learning.
• [IMPLEMENTED_AND_TESTED] Stable LaneSegment IDs, predecessor/successor graph, continuous station.
• [IMPLEMENTED_AND_TESTED] Station-dependent adjacency supports lane births, terminations, and partial neighbor availability.
• [SCRIPTED_ONLY] Smooth adjacent-only trajectory provides bounded lateral motion, commitment, and abort semantics.
• [IMPLEMENTED_AND_TESTED] Isolated Track B did not replace production V5 fixed-path topology.
Station-dependent adjacency
T1
T2
T3
T4
merge lane ends
valid adjacency interval
stable IDs
local adjacency
birth/end
commit/abort
polygon collision
The trajectory layer executes smooth lateral motion; the policy decision was later moved to V6 lane intent.
Notes: Main message: Track B created a lane topology abstraction that can represent lane birth and termination. This solves a precondition for learning: the policy should choose an adjacent intent, while topology determines whether that intent is valid and the trajectory layer realizes the path. Timing: 8:55–9:25 Speaker notes: Track B created a lane topology abstraction that can represent lane birth and termination. This solves a precondition for learning: the policy should choose an adjacent intent, while topology determines whether that intent is valid and the trajectory layer realizes the path. Evidence / source boundary: Master context lines 95–101, 152–160; results/status lines 57–73; technical methodology lines 171–179; Q&A Q116–Q120. Likely audience question: Is LaneSegment deployed in production V5? Concise answer: No. It is implemented and tested in an isolated lane branch. Production V5 remains legacy fixed path.

## Slide 21
LANE / MERGE INFRASTRUCTURE
Merge and left-turn-pocket infrastructure: scripted validation only
21
Scripted demos validated geometry, not learned lane choice.
• [SCRIPTED_ONLY] Merge oracle demo completed in 4.44 s with final lateral offset 3.60 m.
• [SCRIPTED_ONLY] Peak lateral acceleration 1.0635 m/s²; peak lateral jerk 2.5 m/s³; 14 lane tests passed.
• [SCRIPTED_ONLY] Left-turn pocket defines T3 → T2 → T1 → LP and connector to receiving lane.
• [SCRIPTED_ONLY] No pocket PPO ran; scripted merge and pocket routes are not learned behavior.
Scripted merge metrics
Metric
Value
Duration
4.44 s
Offset
3.60 m
Lat accel
1.0635 m/s²
Lat jerk
2.5 m/s³
Learned?
false
Left-turn pocket topology
T4
T3
T2
T1
LP
T3 → T2 → T1 → LP
scripted topology / no pocket PPO
SCRIPTED_ONLY
SCRIPTED_ONLY
Do not describe scripted merge or pocket behavior as learned.
Notes: Main message: This is one of the easiest places to overclaim. The merge oracle and pocket demonstrations validated the topology and trajectory layer. The numerical merge metrics are real scripted infrastructure metrics; learned_policy_used was false. No pocket PPO was performed. Timing: 9:25–9:55 Speaker notes: This is one of the easiest places to overclaim. The merge oracle and pocket demonstrations validated the topology and trajectory layer. The numerical merge metrics are real scripted infrastructure metrics; learned_policy_used was false. No pocket PPO was performed. Evidence / source boundary: Master context lines 95–101; results/status lines 61–73; Q&A Q121–Q130. Likely audience question: Did the policy generate the 4.44-second merge? Concise answer: No. It was a scripted oracle demonstration validating infrastructure and trajectory smoothness.

## Slide 22
V6 LEARNED-MERGE ATTEMPT
V6 hybrid lane-change policy design
22
V6 separated decision ownership: policy chooses lane intent; trajectory layer executes lateral motion.
• [IMPLEMENTED_AND_TESTED] Frozen V5 provides the base longitudinal intersection policy.
• [IMPLEMENTED_AND_TESTED] V6 adds categorical adjacent-lane intent: LEFT, KEEP, RIGHT, with invalid intents masked.
• [IMPLEMENTED_AND_TESTED] A bounded 1-D residual adjusts longitudinal acceleration around the V5 base.
• [REJECTED_CANDIDATE] Mechanics were implemented, but no V6 checkpoint was promoted.
V5 base
frozen
merge context
24 features
V6 heads
trajectory
layer
lane intent
LEFT / KEEP / RIGHT
longitudinal
residual
Why categorical intent?
Topology-level lane decisions should not fight a continuous steering scalar. Smooth lateral realization is deterministic and adjacent-only.
Design was coherent; integrated learning still failed safety/promotion gates.
Notes: Main message: V6 is a clean design choice: freeze V5 longitudinal behavior, add a lane intent head, and use deterministic trajectory execution. This avoids raw steering and lane-change generator conflicts. But design mechanics alone do not imply learned safe merging. Timing: 9:55–10:25 Speaker notes: V6 is a clean design choice: freeze V5 longitudinal behavior, add a lane intent head, and use deterministic trajectory execution. This avoids raw steering and lane-change generator conflicts. But design mechanics alone do not imply learned safe merging. Evidence / source boundary: Architecture evolution lines 90–101; simulator/architecture lines 99–105; master context lines 101–109; Q&A Q041–Q042. Likely audience question: Why categorical lane intent instead of steering? Concise answer: Because lane change is a topology-level adjacent-intent decision. A deterministic trajectory layer can enforce feasible lateral motion once the policy chooses intent.

## Slide 23
V6 LEARNED-MERGE ATTEMPT
Learned-merge result: from KEEP collapse to unsafe exploration
23
Stage 4.2 avoided degeneracy, but unsafe entries and collisions were far beyond gates.
• [REJECTED_CANDIDATE] Initial V6 saved candidates: 0% required open-gap merges and 0% request rate—KEEP collapse.
• [REJECTED_CANDIDATE] Stage 4.1 reached 92.36% offline test accuracy but integrated open-gap completion was 43.17%.
• [IMPLEMENTED_AND_TESTED] `merge_reward_v2` passed all 168 paired reward-order gates; no DAgger/BC/prewarm/oracle loss in Stage 4.2.
• [REJECTED_CANDIDATE] Stage 4.2 PPO-only runs stopped at 2,048 steps: unsafe entry 23.17/24.05%, collisions 11.84/16.00%.
• [INCONCLUSIVE] No checkpoint saved/promoted; future-final bank not run.
Initial V6
0% merge
0% request
KEEP collapse
REJECTED
CANDIDATE
Stage 4.1
92.36% offline
17.36% unsafe
reward/action mismatch
REJECTED
CANDIDATE
Stage 4.2
97.37/96% open
23–24% unsafe
nondegenerate but unsafe
REJECTED
CANDIDATE
Stage 4.2 early gate table
Main: 97.37% open completion, 23.17% unsafe, 11.84% collision.
Fallback: 96.00% open completion, 24.05% unsafe, 16.00% collision.
NO CHECKPOINT PROMOTED
Stage 4.2 used mandatory PPO-only runs; no DAgger, behavior cloning, prewarming, or supervised oracle-action loss.
Notes: Main message: This slide summarizes the lane-learning arc. Initial V6 collapsed to KEEP. Stage 4.1 improved offline lane classification but failed integrated behavior and revealed reward inversion. Stage 4.2 fixed reward ordering and produced nontrivial LEFT actions, but it was unsafe and stopped before any saved checkpoint. Timing: 10:25–11:10 Speaker notes: This slide summarizes the lane-learning arc. Initial V6 collapsed to KEEP. Stage 4.1 improved offline lane classification but failed integrated behavior and revealed reward inversion. Stage 4.2 fixed reward ordering and produced nontrivial LEFT actions, but it was unsafe and stopped before any saved checkpoint. Evidence / source boundary: Master context lines 103–109; results/status lines 77–111; Q&A Q123–Q125, Q131–Q135. Stage 4.2 rule: no DAgger/BC/prewarm/oracle-action loss. Likely audience question: Is Stage 4.2 a success because it avoided KEEP collapse? Concise answer: No. Non-degeneracy is only one condition. Unsafe entry and collision rates failed early gates, so there was no checkpoint and no promotion.

## Slide 24
STATUS / PLAN
Current status matrix and next technical plan
24
The project ends with an immutable V5 baseline and a sharply localized lane-learning plan.
• [PRODUCTION] Immutable V5 + `crosswalk_wide_v1` + `legacy_path_v1` + `jerk_limited_v1`.
• [TRAINING_ONLY] V2.1 is available only as a future training environment.
• [SCRIPTED_ONLY] Merge oracle/demo and pocket routes validate infrastructure only.
• [REJECTED_CANDIDATE] No V5.1 or V6 checkpoint promoted; final banks not run after failed gates.
• [PLANNED] Stage 4.3: PPO-only, safer nondegenerate prior, 1:1 safe/unsafe eligible-decision curriculum.
Status
Items
PRODUCTION
V5 checkpoint; crosswalk-wide; legacy path; jerk-limited dynamics
TRAINING_ONLY
Predictive pedestrian V2.1
IMPLEMENTED
LaneSegment; trajectory; V6 mechanics; merge_reward_v2
SCRIPTED_ONLY
Merge oracle/demo; left-turn pocket routes
REJECTED
Ped V1/V2; all V5.1; all V6
PLANNED
Stage 4.3 controlled PPO-only merge experiment
Stage 4.3 must keep fixed
reward V2 • topology • frozen V5 base • 24-feature context • runtime action path • safety gates
Gate before final bank
non-degeneracy + opportunity use + unsafe choice + collisions + V5 regression
Future work should run final banks only after earlier gates pass.
Notes: Main message: This status matrix is the defense against overclaiming. The production anchor remains V5. V2.1 is training-only. Lane topology is implemented and tested, but merge and pocket demos are scripted. All V5.1 and V6 candidates are rejected. Stage 4.3 is a plan, not a result. Timing: 11:10–12:05 Speaker notes: This status matrix is the defense against overclaiming. The production anchor remains V5. V2.1 is training-only. Lane topology is implemented and tested, but merge and pocket demos are scripted. All V5.1 and V6 candidates are rejected. Stage 4.3 is a plan, not a result. Evidence / source boundary: Master context lines 150–160; results/status lines 113–124; technical methodology lines 181–193; Q&A Q146–Q149. Likely audience question: What exactly runs today? Concise answer: V5 with graph observations, jerk-limited longitudinal dynamics, conservative crosswalk-wide pedestrian mode, and legacy fixed paths.

## Slide 25
CONCLUSION
Key takeaways and future direction
25
The durable result is an auditable way to add driving complexity without confusing policy, simulator, and script.
• [IMPLEMENTED_AND_TESTED] Built a reproducible multi-agent intersection research platform.
• [PRODUCTION] Produced a qualified V5 shared graph longitudinal policy for the declared simulator scope.
• [IMPLEMENTED_AND_TESTED] Added jerk-limited dynamics and stopping-feasibility reasoning to make labels and rewards more honest.
• [IMPLEMENTED_AND_TESTED] Created lane topology/trajectory foundation for future lane-intent learning.
• [REJECTED_CANDIDATE] Used negative results to localize remaining issues: pedestrian conservatism, longitudinal retention, and safe nondegenerate merge.
Retain
Immutable V5
policy-owned
qualification
Improve
Pedestrian realism
longitudinal retention
lane intent safety
Validate
Separated seeds
hard gates
final bank only after pass
Closing statement
The internship’s strongest contribution is not one checkpoint; it is a disciplined evidence chain for adding interaction complexity while preserving claim ownership.
Appendix contains exact metrics, equations, Q&A, and safe/unsafe claim language.
Notes: Main message: End with three contributions: the simulator/evaluation platform, the qualified V5 graph policy with jerk-limited dynamics, and the status discipline that rejected unsafe candidates. The future direction is to make lane intent safe without losing the evidence chain. Timing: 12:05–12:40 main talk + discussion buffer Speaker notes: End with three contributions: the simulator/evaluation platform, the qualified V5 graph policy with jerk-limited dynamics, and the status discipline that rejected unsafe candidates. The future direction is to make lane intent safe without losing the evidence chain. Evidence / source boundary: Brief/story lines 102–112; master context lines 121–133, 150–160; Q&A Q150. Likely audience question: What are you most proud of? Concise answer: Making the system and its claims auditable—especially retaining V5 when later experiments improved one metric but failed the complete standard.

## Slide 26
APPENDIX / TECHNICAL BACKUP
A1 — Exact V5 release metrics and gates
26
V5 production identity and release-claim metrics.
Item
Value
Checkpoint
yield_kinodynamic_v5_combined_production.npz
SHA-256
e0c5a656eda95915db0b33aab86e8c2779c85c53b4f401c6b880725649aa0cba
Gates
completion ≥90%; collision-event ≤1%; involved ≤2%; other ≤3%
Qualification
30/30 groups passed
Group
Completion
Collision events
Collided vehicles
Other violations
Sparse 3 lanes / 12 cars
99.72%
0.00%
0.00%
0.28%
Dense 3 lanes / 24 cars
96.67%
0.63%
1.25%
1.88%
Stress 3 lanes / 36 cars
92.22%
0.56%
1.11%
2.64%
PRODUCTION
Production means accepted simulator checkpoint/configuration, not road deployment.
Notes: Main message: This backup slide contains the exact production checkpoint identity, gates, and combined group metrics. Use it if asked for numerical evidence. Speaker notes: This backup slide contains the exact production checkpoint identity, gates, and combined group metrics. Use it if asked for numerical evidence. Evidence / source boundary: Results/status lines 5–13; master context lines 13 and 67–75. Likely audience question: What are the qualification thresholds? Concise answer: Per group: completion at least 90%, collision-event at most 1%, involved vehicles at most 2%, and other violations at most 3%.

## Slide 27
APPENDIX / TECHNICAL BACKUP
A2 — V5 tensor and actor detail
27
Production tensor contract and actor heads.
Property
Value / boundary
Status
Ego / node / edge
49 / 27 / 25
PRODUCTION
Max nodes
52 in selected checkpoint
PRODUCTION
Hidden size
128
PRODUCTION
Attention blocks
2 custom typed graph-attention blocks
PRODUCTION
Longitudinal modes
brake / creep / go with learned mixture gate
PRODUCTION
Action 0
normalized longitudinal acceleration
PRODUCTION
Action 1
steering output retained but inert/path-locked
LIMITATION
Runtime shield
off in formal qualification
PRODUCTION
Do not claim learned V5 lateral control.
Notes: Main message: This slide backs up architecture questions. The steering caveat is part of the claim: the second action exists for compatibility but does not control lateral motion in V5. Speaker notes: This slide backs up architecture questions. The steering caveat is part of the claim: the second action exists for compatibility but does not control lateral motion in V5. Evidence / source boundary: Architecture evolution lines 54–88; simulator/architecture lines 47–85. Likely audience question: Does action dimension 2 mean learned steering? Concise answer: No. Action 1 exists but Vehicle.step resets steering and lateral offset to zero under the path-locked V5 contract.

## Slide 28
APPENDIX / TECHNICAL BACKUP
A3 — Dynamics equations and stopping feasibility
28
Jerk-aware stop distance can differ sharply from v²/(2b).
• Request scaling: u ≥ 0 → 2.5u m/s²; u < 0 → 4.0u m/s².
• Jerk selection: J = 3.0 m/s³ when increasing acceleration; J = 6.0 m/s³ when decreasing/braking.
• Discrete integration uses trapezoidal average acceleration and average speed at dt = 0.2 s.
• Example: v₀=4, a₀=+2, b=4, J=6 gives 5.125 m vs 2.0 m instant-brake estimate.
a_req = u·2.5 if u≥0; u·4.0 if u<0
Δa = clip(a_req − a_t, −JΔt, JΔt)
a_{t+1}=a_t+Δa
v_{t+1}=clip(v_t+(a_t+a_{t+1})Δt/2,0,13.4)
s_{t+1}=s_t+(v_t+v_{t+1})Δt/2
instant
2.0 m
jerk-aware
5.125 m
v=4 m/s, a=+2 m/s², brake=4 m/s², J=6 m/s³
These are simulator parameters, not universal vehicle limits.
Notes: Main message: Use this slide for equation questions. The central point is not smoothness alone; actuator-aware feasibility changes labels and rewards. Speaker notes: Use this slide for equation questions. The central point is not smoothness alone; actuator-aware feasibility changes labels and rewards. Evidence / source boundary: Technical methodology lines 87–133; master context lines 61–63. Likely audience question: Why does jerk matter for stopping labels? Concise answer: Because a vehicle already accelerating needs distance to ramp into braking before full comfortable braking is available.

## Slide 29
APPENDIX / TECHNICAL BACKUP
A4 — PPO, prewarm, and provenance rule
29
Promoted learned behavior required positive PPO and independent deterministic qualification.
• PPO with γ = 0.99, GAE λ = 0.95, clipped policy objective, value loss, entropy, and stage-specific auxiliary/retention terms.
• V5 selected lineage: 51,200 PPO environment steps; 500 bounded prewarm steps only in ROR stage.
• Prewarm, gate CE, physics targets, reference KL, and labels are optimizer-only supports.
• Stage 4.2 explicitly used mandatory PPO-only runs: no DAgger, behavior cloning, prewarm, or supervised oracle-action loss.
• Formal evaluation: deterministic policy output, no runtime acceleration shield, separated seeds, hard gates.
Provenance rule
prewarm-only
TRAINING_ONLY / DIAGNOSTIC_ONLY
positive PPO + focused success
LEARNED_PARTIAL
failed any required group
REJECTED_CANDIDATE
passed every preregistered group
PRODUCTION
Formal runtime ≠ pure tabula-rasa RL
Correct wording: PPO-trained learned policy with no runtime action override in qualification.
Do not call prewarm-only artifacts reinforcement-learned.
Notes: Main message: This appendix slide is for methodology questions about PPO purity, prewarm, and Stage 4.2. It states exactly what support existed and what did not. Speaker notes: This appendix slide is for methodology questions about PPO purity, prewarm, and Stage 4.2. It states exactly what support existed and what did not. Evidence / source boundary: Technical methodology lines 145–159; training curriculum lines 38–45; Q&A Q055–Q078. Likely audience question: Is production V5 pure RL? Concise answer: Runtime decisions are policy-owned, but V5 used engineered observations/rewards and a bounded ROR prewarm before PPO. Avoid philosophical purity claims.

## Slide 30
APPENDIX / TECHNICAL BACKUP
A5 — Pedestrian model decision table
30
Pedestrian alternatives were implemented, but only V2.1 was retained as training-only.
Model
Mechanism
Result
Decision
crosswalk_wide_v1
broad route-associated crosswalk conflict
V5 production groups passed; conservative overblocking
PRODUCTION
V1 corridor
swept route corridor + temporal occupancy
30/30 original passed; dense/stress holdouts failed other/collision gates
REJECTED
V2 waiting
waiting WALK-permitted activation + brake-now feasibility
fixed two traces; five V2-only ped-yield identities + one reordered collision
REJECTED
V2.1 imminent
bounded imminent-WALK branch inside stopping horizon
seed 66827 corrected with positive margin; not promoted
TRAINING_ONLY
Safe wording
V2.1 is the best accepted training-only pedestrian-conflict environment; production stayed crosswalk_wide_v1.
Do not describe V2.1 as production.
Notes: Main message: This table supports detailed pedestrian questions. It records what each model changed and why the decision boundary stayed conservative. Speaker notes: This table supports detailed pedestrian questions. It records what each model changed and why the decision boundary stayed conservative. Evidence / source boundary: Results/status lines 32–41; technical methodology lines 135–143; Q&A Q091–Q095. Likely audience question: Why was V2.1 not production if it fixed seed 66827? Concise answer: Because a targeted fix is not a complete promotion. It was frozen as training-only, and production remained crosswalk-wide.

## Slide 31
APPENDIX / TECHNICAL BACKUP
A6 — V5.1 diagnostics and candidate outcomes
31
V5.1 was rejected because improvements traded off against retention and category gates.
Audit class
Count
Queue-chain
85
Insufficient brake component
77
Mixture-gate dilution
74
Late environment / observation signal
39
Policy reaction delay
2
Total
277
Run
Key outcome
Decision
Stage 3B-2A
collisions improved; other violations 3.19–3.33% vs 3% gate
REJECTED
Stage 3B-2A2 main
40,960 steps; stress 91.39% / 1.204% / 2.407% / 3.333%
REJECTED
PPO-only fallback
original groups passed; complete diagnosis left/ped retention failed
REJECTED
Final bank
not run after earlier failures
NOT RUN
NO V5.1 PROMOTION
Negative result: isolated metrics improved, but full evidence standard failed.
Notes: Main message: Use this slide if asked for the detailed V5.1 rejection rationale. It combines the failure taxonomy and the candidate-level decisions. Speaker notes: Use this slide if asked for the detailed V5.1 rejection rationale. It combines the failure taxonomy and the candidate-level decisions. Evidence / source boundary: Results/status lines 17–28 and 45–56; Q&A Q113–Q115, Q139. Likely audience question: Why was the final bank not run? Concise answer: Candidates failed earlier gates, so running the final bank would have violated the staged evaluation protocol and risked post-hoc selection.

## Slide 32
APPENDIX / TECHNICAL BACKUP
A7 — Track B lane test inventory
32
Track B validated topology and trajectory mechanics, not learned lane decisions.
• Stable LaneSegment IDs and graph connectivity.
• Station-dependent adjacency; lane birth and termination; continuous station.
• Adjacent-only transition; commitment/abort state; smooth bounded lateral trajectory.
• Polygon collision checks and deterministic merge oracle.
• Left-turn pocket topology and connector suites; no learned pocket policy.
Scripted merge metric
Value
Accepted/completed
true / true
Duration
4.44 s
Final lateral offset
3.60 m
Peak lateral acceleration
1.0635 m/s²
Peak lateral jerk
2.5 m/s³
Learned policy used
false
Lane tests
14 passed
SCRIPTED_ONLY
Do not call Track B scripted merge learned.
Notes: Main message: This is the backup for lane infrastructure questions. It lists the tested components and the exact scripted merge metrics. Speaker notes: This is the backup for lane infrastructure questions. It lists the tested components and the exact scripted merge metrics. Evidence / source boundary: Results/status lines 57–73; technical methodology lines 171–179; Q&A Q116–Q122. Likely audience question: Do the 14 tests prove learned merge readiness? Concise answer: No. They support implementation correctness for topology and trajectory mechanics, not learned policy safety.

## Slide 33
APPENDIX / TECHNICAL BACKUP
A8 — V6 failure chain and Stage 4.3 plan
33
The merge result localized the next experiment instead of producing a promotable checkpoint.
Initial V6
KEEP collapse
0% required merges
bias / weak prewarm / coverage
REJECTED_CANDIDATE
Stage 4.1
92.36% offline accuracy
43.17% open completion
17.36% unsafe
offline ≠ integrated safety; reward inversion
REJECTED_CANDIDATE
Stage 4.2
168 reward gates passed
97.37/96% open completion
23–24% unsafe
nondegenerate but unsafe; stopped at 2,048
REJECTED_CANDIDATE
Stage 4.3
safer prior + 1:1 safe/unsafe
PPO-only curriculum
planned; no result yet
PLANNED
Critical Stage 4.2 caveat
No DAgger, no behavior cloning, no oracle prewarm, no supervised oracle-action loss; PPO-only runs failed early gates before checkpoint save.
Future-final bank not run.
Notes: Main message: This slide supports merge follow-up questions. The key is not to call Stage 4.2 successful. It is a localized partial learning signal with failed safety. Speaker notes: This slide supports merge follow-up questions. The key is not to call Stage 4.2 successful. It is a localized partial learning signal with failed safety. Evidence / source boundary: Results/status lines 77–111; master context lines 103–109 and 160; Q&A Q131–Q135, Q146–Q149. Likely audience question: What did Stage 4.2 prove? Concise answer: It proved the system no longer collapsed to KEEP and could learn nontrivial LEFT behavior, but it also proved the early policy was unsafe and non-promotable.

## Slide 34
APPENDIX / TECHNICAL BACKUP
A9 — Status label definitions
34
These labels are part of the claim language, not cosmetic tags.
Label
Meaning in this deck
PRODUCTION
Accepted repository simulator checkpoint/configuration after required gates; not road deployment.
IMPLEMENTED_AND_TESTED
Code/mechanics/tests exist, but not necessarily promoted as final learned behavior.
TRAINING_ONLY
May support future optimization; not formal production runtime.
SCRIPTED_ONLY
Deterministic oracle or demo; not learned behavior.
LEARNED_PARTIAL
Positive learning signal under limited focus, not promoted.
REJECTED_CANDIDATE
Tested candidate failed at least one required gate or criterion.
DIAGNOSTIC_ONLY
Analysis/counterfactual/taxonomy used to localize issues, not a deployable result.
PLANNED
Recommended next experiment; not executed result.
INCONCLUSIVE
Not verified by repository evidence; may be user-provided narrative or missing artifact.
Use the label with the claim every time; do not move facts across status boundaries.
Notes: Main message: Use this slide if the audience asks how to interpret labels. It makes the deck’s claim grammar explicit. Speaker notes: Use this slide if the audience asks how to interpret labels. It makes the deck’s claim grammar explicit. Evidence / source boundary: Master context lines 3, 121–148; results/status lines 115–125. Likely audience question: Why is “production” potentially confusing? Concise answer: Because outside this project it may imply road deployment. Here it only means the accepted simulator artifact under declared gates.

## Slide 35
APPENDIX / TECHNICAL BACKUP
A10 — Q&A: world model and pivot
35
Short answers for likely questions about the original direction.
Was DreamerV3 trained successfully?
[INCONCLUSIVE] No repository evidence supports a successful training run.
Was the pivot a failure?
[IMPLEMENTED_AND_TESTED] No; it converted an oversized goal into a reproducible simulator-policy program.
Are the world-model and V5 systems connected in code?
[INCONCLUSIVE] No code-level connection is evidenced in the handoff.
What is the safe Dreamer claim?
[INCONCLUSIVE] The internship began with a DreamerV3/world-model direction and pivoted before a repository-verified result.
Avoid: “Dreamer failed,” “Dreamer generated scenarios,” or “V5 uses Dreamer.”
Notes: Main message: This appendix slide distills the Q&A bank for the initial world-model topic. Speaker notes: This appendix slide distills the Q&A bank for the initial world-model topic. Evidence / source boundary: Q&A bank Q001–Q008; master context lines 7–21 and 137–138. Likely audience question: What should be avoided? Concise answer: Any claim that DreamerV3 was trained, modified, benchmarked, or used by V5, because the handoff does not verify those artifacts.

## Slide 36
APPENDIX / TECHNICAL BACKUP
A11 — Q&A: policy ownership, shield, and production
36
Short answers for likely methodology questions.
Is production V5 runtime shielded?
[PRODUCTION] Formal qualification used no runtime acceleration override; environment semantics still exist.
Is production V5 pure RL?
[PRODUCTION] Runtime decisions are policy-owned, but the lineage used engineered observations/rewards and bounded ROR prewarm.
Are signal rules learned?
[PRODUCTION] Signal/legal context is simulator-defined; the policy learns the longitudinal response.
What is the largest production limitation?
[PRODUCTION] V5 is longitudinal/path-locked; steering output is inert.
Avoid: “no engineered safety logic anywhere” or “pure RL with no prior knowledge.”
Notes: Main message: This slide collects short answers around the most sensitive methodology claim: policy-owned runtime without pretending the environment is unengineered. Speaker notes: This slide collects short answers around the most sensitive methodology claim: policy-owned runtime without pretending the environment is unengineered. Evidence / source boundary: Q&A bank Q067–Q078, Q096–Q100, Q141–Q142. Likely audience question: Does no runtime shield mean no safety constraints? Concise answer: No. It means no acceleration action override in formal qualification; routes, physics, legal semantics, and event truth are still simulator code.

## Slide 37
APPENDIX / TECHNICAL BACKUP
A12 — Q&A: lane, merge, and left-turn pocket
37
Short answers for likely lane-branch questions.
Did the scripted merge work?
[SCRIPTED_ONLY] Yes as infrastructure validation, with learned_policy_used=false.
Did V6 learn safe merging?
[REJECTED_CANDIDATE] No; Stage 4.2 avoided collapse but failed unsafe-entry and collision gates.
What happened in the first learned merge attempt?
[REJECTED_CANDIDATE] Deterministic candidates selected KEEP everywhere: 0% required merges and requests.
Was the left-turn pocket learned?
[SCRIPTED_ONLY] No; topology and routes were deterministic, and no pocket PPO ran.
Why is V6 still useful?
[LEARNED_PARTIAL] It localized failure to hybrid lane intent, reward alignment, action coupling, and rollout coverage.
Avoid: “scripted merge learned,” “left pocket learned,” or “V6 safe merge promoted.”
Notes: Main message: This Q&A slide protects against overclaiming lane work. It separates implemented topology, scripted validation, partial learned exploration, and rejected candidates. Speaker notes: This Q&A slide protects against overclaiming lane work. It separates implemented topology, scripted validation, partial learned exploration, and rejected candidates. Evidence / source boundary: Q&A bank Q116–Q135. Likely audience question: What is actually learned in merge? Concise answer: Stage 4.2 learned nontrivial lane-intent behavior, but not a safe or promotable merge policy.

## Slide 38
APPENDIX / TECHNICAL BACKUP
A13 — Safe claims / unsafe claims
38
Use safe wording that matches the evidence boundary.
Safe claim
Unsafe wording to avoid
The internship began with a DreamerV3/world-model direction and pivoted because scope was too large.
DreamerV3 was successfully trained or benchmarked.
The selected V5 checkpoint passed all 30 declared simulator qualification groups.
V5 solves autonomous driving or is road-production-ready.
V5 is a graph actor-critic for path-locked longitudinal intersection control.
V5 learned steering or lane changing.
V2.1 is a training-only pedestrian environment.
V2.1 is production.
Merge and pocket demos validate scripted infrastructure.
Scripted merge or pocket routes were learned.
V5.1/V6 candidates were rejected; final banks were not run after failed gates.
V5.1 or V6 was promoted, or final bank confirmed the result.
This slide is intentionally conservative; it is designed for Q&A defense.
Notes: Main message: This is the final claim-safety backup slide. It should be used if asked how to phrase results in a report or defense. Speaker notes: This is the final claim-safety backup slide. It should be used if asked how to phrase results in a report or defense. Evidence / source boundary: Master context lines 121–148; claim/evidence CSV. Likely audience question: What is the most dangerous overclaim? Concise answer: Calling scripted or training-only behavior learned/production, or implying V5.1/V6 were promoted or final banks were run.

## Slide 39
APPENDIX / TECHNICAL BACKUP
A14 — Selected background references
39
These papers motivate the background; they are not claimed baselines for the internship experiments.
[R1] Hafner et al. (2023)
DreamerV3: Mastering Diverse Domains through World Models
arXiv:2301.04104
[R2] Xu et al. (2022)
SafeBench: Benchmarking Platform for Safety Evaluation of Autonomous Vehicles
arXiv:2206.09682
[R3] Zhou et al. (2020)
SMARTS: Scalable Multi-Agent RL Training School for Autonomous Driving
arXiv:2010.09776
[R4] Vinitsky et al. (2022)
Nocturne: scalable driving benchmark for multi-agent learning
arXiv:2206.09889
[R5] Gulino et al. (2023)
Waymax: Accelerated Data-Driven Simulator for AV Research
arXiv:2310.08710
[R6] Liang et al. (2020)
LaneGCN: Learning Lane Graph Representations for Motion Forecasting
ECCV / arXiv:2007.13732
[R7] Schulman et al. (2017)
Proximal Policy Optimization Algorithms
arXiv:1707.06347
Reference boundary
The deck uses these papers for background framing only. All internship performance numbers come from the uploaded handoff evidence files.
Add full BibTeX from these arXiv/venue entries if the final report requires formal citations.
Notes: Main message: This references slide satisfies the requested background/prior-work support. It does not imply experimental comparison against these works. Speaker notes: This references slide satisfies the requested background/prior-work support. It does not imply experimental comparison against these works. Evidence / source boundary: External paper references searched from arXiv/venue pages; internship metrics remain from handoff files. Likely audience question: Which reference is most directly tied to the original objective? Concise answer: DreamerV3 for world-model imagined rollouts, plus SafeBench for safety-critical scenario evaluation.